| 10 Security If you are using your Network Remote Control BaseCam wirelessly, we recommend you change the password from its default for security reasons. To change the password, click the Change Password link on the left side of the browser screen. 11 Limitations This version has no way of controlling the zoom, focus and aperture of the camera, even if you have a camera that had these features. Not applicable for critical usage or hazardous environments. Operate at temperatures between 32ºF and 132ºF (0ºC and 55ºC) only. This device is designed for indoor use only. 12 Extra Mounting Hardware Top: Tripod mount fastened with screw legs. Bottom: Screw legs for height adjustment |  | Network Remote Control BaseCam( QuickStart Guide Thank you for purchasing a Network Remote Control BaseCam. The intent of this document is to get you up and running as quickly as possible. For a fuller explanation of the features and controls please refer to the help page on our web site. 1 What’s in the box? The package contains the following items: 1 Remote Control BasePod( motorized base 1 Logitech( webcam 1 USB cable 1 Warranty cards 2 Screw legs 1 Tripod mount Included or shipped separately: 1 Compex NetPassage( NP26G-USB 2 What Does It Do? This package acts a pan/tilt webcam that you view and control remotely. The Logitech webcam is the camera. The Remote Control BasePod is a motorized base that pans and tilts the camera. The NP26G-USB sends camera video and receives movement commands, either wirelessly or over a wired LAN. 3 Before You Begin If you want to use your Network Remote Control BaseCam wirelessly, you need to have a wireless 802.11 network up and running at your site before you begin. To use the Network Remote Control BaseCam via wired connection, you need to have an Ethernet-based LAN up and running at your site. You also need an Ethernet cable to connect the NP26G-USB to one of your network outlets. |
| --- | --- | --- |

| 4 Mounting the QuickCam to the Remote Control BasePod Mount the Logitech QuickCam onto the Remote Control BasePod by completing the following steps. Screw the camera shoe onto the camera as illustrated. Snap camera and attached shoe to Remote Control BasePod’s neck. Line up the camera’s line of sight with the collar’s forward arrow and snap the camera and attached shoe onto the neck. Guide the QuickCam’s USB cable through the passages along the sides and front of Remote Control BasePod’s collar. This will prevent the cable from interfering with the camera’s pan and tilt movements. . |  | 5 Connecting Devices Together Connect the QuickCam and the Remote Control BasePod to the NP2G-USB by completing the following steps. Connect the QuickCam’s USB cable to one of the two USB ports on the back of the NP2G-USB. (The USB ports are the thin rectangular ports.) Connect the square end of the USB cable shipped with the Remote Control BasePod to the port on the back of the Remote Control BasePod. Connect the other end of the USB cable to the second USB port on the back of the NP2G-USB router. 6 Powering Up Connect NP2G-USB’s power cable to the round socket on the back and plug the other end into a power socket. Check whether the USB indicator light on the front of the NP2G-USB comes on. If it does not, you need to update the NP2G-USB’s firmware by following the additional instruction found at http://www.Remote Control Basecam.com/TCamWeb/wifi/webcamguide.htm 7 Wired or Wireless? You can use your Network Remote Control BaseCam either wirelessly or via a wired LAN. To use a wired LAN, you need to connect an Ethernet cable to one of the Ethernet sockets on the back of the NP2G-USB. Connect the other end to a LAN socket. To use your Network Remote Control BaseCam wirelessly, you need to have an existing wireless 802.11 network running at your site. The NP2G-USB will link itself to your network automatically and select the speed, up to 54Mbit. 8 Determining Your Network Remote Control BaseCam’s URL You use your Network Remote Control BaseCam by browsing to its URL using Internet Explorer on a PC connected to the same network. To determine the URL, follow the directions at: http://www.Remote Control Basecam.com/TCamWeb/wifi/WebcamIP.htm 9 Using Your Remote Control BaseCam Wireless From a computer connected to your LAN, browse to the URL you determined in Step 6. The default password is “password.” When you log in, click the Webcam link. Click OK when prompted whether to load an ActiveX control. Your browser then shows the camera’s video stream. To pan and tilt the camera, click the arrow buttons on the screen. |
| --- | --- | --- |

# Text boxes

Camera

Camera

Shoe

Neck

Camera’s

USB cable

Arrow on Collar