| 8 Extra Mounting Hardware Top: 2 Screw legs for height adjustment. Bottom: Tripod mount fastened with screw legs. |  | Remote Control Base-IR® QuickStart Guide IR = Infrared Thank you for purchasing a Remote Control Base-IR. The intent of this document is to get you up and running as quickly as possible. For a fuller explanation of the features and controls please refer to our web site: Help section 1 What’s in the box? The package contains the following items: 1 Remote Control Base-IR motorized base 1 Universal Remote Control 2 AAA batteries 1 Warranty card 2 Screw legs 1 External Power Supply 1 Camera shoe 1 Tripod Mount A camera is not included with this package. 2 What Does It Do? Remote Control Base-IR is a remote-controlled pan/tilt unit for any camera weighing less than ¾ lb. with a standard ¼” #20 tripod mount. The Remote Control Base-IR is a motorized base that pans and tilts the camera. The included TV style remote control is used to pan and tilt the unit using the number buttons. 3 Before You Begin Insert 2 fresh AAA batteries into the included remote control unit. Verify that the top right LED lights when number pad buttons are pressed. Unwrap the included external power supply. Verify that its input voltage range includes the voltage of your electrical wall outlets. If it does, plug the external power supply unit into an electrical outlet. It is possible for the voltage to match but the plug not to fit. In this case a plug adaptor is required but a transformer is not required. Plug the small connector on the end of the power supply cable into the back of the Remote Control Base-IR. Verify that the lights on the Remote Control Base-IR light briefly when power is applied. |
| --- | --- | --- |

| 4 Mounting your camera to the Remote Control Base Mount your camera onto the Remote Control Base-IR by completing the following steps. Screw the camera shoe onto the camera as illustrated. Snap camera and attached shoe to Remote Control Base’s neck. Line up the camera’s line of sight with the collar’s forward arrow and snap the camera and attached shoe onto the neck. If your camera has cables, guide them through the passages along the sides and front of Remote Control Base’s collar. This will prevent the cables from interfering with the camera’s pan and tilt movements. . |  | 5 Testing default operation When the Remote Control Base-IR has power and the remote control unit has fresh batteries, pressing a number button (1 to 9) on the remote should cause the Remote Control Base-IR to move in the direction suggested by the number button’s position relative to the center 5 button. If there is no movement or the lights on the Remote Control Base-IR do not flash when you press buttons 1 to 9, the remote may need to be programmed. To program the remote for default operation, press and hold the SET and TV buttons simultaneously until the LED remains on. Then press 0/10 three times. The LED should turn off, indicating that the remote has been programmed. Pressing a number button (1 to 9) now cause the Remote Control Base-IR to move. Pressing the 5 button should cause the Remote Control Base-IR to move to the Center position. 6 Using your own Universal Remote Control The remote control unit supplied with this package has limited range. If you have your own Universal Remote Control, you may prefer to use that to control your Remote Control Base-IR. The following steps are OPTIONAL. The Remote Control Base-IR will accept standard SONY® TV numeric commands. Consult your Universal Remote Control’s instructions if you do not know how to program it. Your Universal Remote Control’s instructions should also indicate the code to use for SONY TVs. The code is usually 000, 001, or 002. 7 Reprogramming your Remote Control Base-IR for different buttons CAUTION: The following steps are OPTIONAL and for advanced users only. You may wish to make your Remote Control Base-IR respond to different buttons on your remote control unit. Start by making sure your remote control is sending SONY TV commands. Enter programming mode on the Remote Control Base-IR by pressing and holding the Pupil Button for 2 seconds. You may need to use the back of a pen or pencil. Do not scratch or mark the surface of the button, as it is also the IR sensor. The UP arrow will flash to indicate programming mode. Press the remote control button you would like to control the UP direction. If the command is accepted, the LEFT and UP arrows will flash. Press the button on your remote you would like to control the diagonal UP, LEFT direction. Continue in this manner until all 4 direction arrows flash. Finally press the button you would like to use for the Center position. After this command is accepted, the Remote Control Base-IR will exit programming mode. If Remote Control Base-IR power is lost during programming, the Remote Control Base-IR will revert to original factory set default programming. |
| --- | --- | --- |

# Text boxes

Pupil Button  Universal Remote Control’s instructions ar

Arrow on Collar arUniversal Remote Control’s instructions ar

Camera’s

cable

Neck

Camera

Shoe

Camera